Measuring tune coupling in
LHC using the BBQ system

---
Beam1
Δy = 2.8°
Δx = 3.6°

---
Beam 2
Δx = 15.3°, Δy = 10.7°
Δy = 57.8°
Δx = 98.4°

---
Data Acquisition
- Data read in directly through the JAPC interface.
- Not a continues stream. Has to be “ cut and glued” to be turn by turn data.
To turn by
turn data
Find
synchronization
Calculate
coupling

---
To turn by turn data
- Some of the data is read in twice.
- This enable us to construct the turn by turn data.

---
Find synchronization
- The two BBQs are not synchronized by default.
- Two ideas how to synchronize them.
  1. Use injection.
  2. Model dependent synchronization.

---
From injection

---
Model depended
Step 1: shift the phase (from model) of FFT1 to the same as FFT2.
This is done in the frequency domain and the signal is then transformed back to the time domain.
Step2: Move one of the signal along the other and evaluate the difference.

---
Some difficulties
If the modulation is periodic it is hard to find the real synchronization.

---
Some difficulties
- A couple of turns after. Almost as good.
- Also sensitive that the phase advance from the model is correct.

---
Calculate coupling
- Output the synchronized data.
- Runs Drive.
- Runs GetLLM
- Import the data.
- Present it and calculate the statistical error-bars.

---
Displaying the results

---
First results

---
First result zoomed

---
Conclusion
- At the moment the only way to be 100% sure on the synchronization is to use either kick or injection.
- The first results seems to be in good agreement with the measurements from the AC-dipole.

---
Outlook
- We will have to possibility to analyze the injection oscillations, for the pilot beam, measured by the normal BPM.
- With this we can get statistic over the drifts in the machine but will also be excellent for comparing the result with the BBQ.
- Read in to an on-line buffer, use the injection to synchronize and as long as we have reading we can construct the turn by turn data and hence know that the synchronization is correct.

---
How to proceed (1)
1. Automatic save all the oscillation data for both the BBQ and the normal BPM. Compare the results from those. (This should be possible to start already next week)
2. Fully automatized analysis of the injection oscillations. (1 month)
3. Implement the buffer so the incoming data is always synchronized (1 month).
4. Try to identify when we can get good measurements with the system for other settings then injection. When do we have to chirp and so on. Compare it with results from the AC-dipole. (Guess next MD, can be done parasitically )

---
How to proceed (2)
5. Investigate the possibility to use other pickups then the BBQ for online coupling measurements. Particular interesting for B1 since the BBQ are placed “wrongly”.
6. Provide a fully automatized online measurement of the coupling including the phase. (hopefully end of summer)
7. Possibly have like a “correct button” that calculates the correction and sends them.